## Slide 1: Chemical Tankers Operation
Preparation for cargo operation : Chemical tanker safety procedure

## Slide 2: Ship checks prior to arrival
When approaching a port to load or discharge cargo, the following important checks should be made by the ship in time to allow any necessary work to be done:
On tanks in which cargo is to be transferred, in-tank instrumentation such as level gauges, level alarms and thermometers should be tested for operation and accuracy, and remote system controls tested where appropriate. High level alarms and tank overflow control alarms are safety critical components of the cargo transfer system, and loading should not commence if pre-transfer checks find them at fault.

## Slide 3: Ship checks prior to arrival
Hatches, lids and openings to cargo tanks that are not required to be open for a specific reason should be firmly closed.
Cargo pipelines and crossover valves should be checked, and all drains closed and secured.
All ship's cargo and bunker pipelines not in use should be securely blanked and fully bolted at the manifold. Unless it is to be used,

## Slide 4: Ship checks prior to arrival
Where loading or discharging is to be via a cargo pump-room, the pump-room ventilation system should be checked to ensure readiness for operation throughout the cargo operations.
Cargo area deck lighting should be checked and confirmed as being in full working order, with special attention given to the area of the ship to shore cargo connection and hose handling equipment.

## Slide 5: Ship checks after arrival but prior to cargo operations
Before any cargo transfer starts, the responsible officer should be satisfied that the applicable precautions are being observed. The use of safety checklists, appropriately adapted for the specific ship, is strongly recommended. The following important checks should be made by the ship at this stage:
Information should be sought on any forecast of adverse weather conditions which may require operations to be stopped or transfer rates reduced.

## Slide 6: Ship checks after arrival but prior to cargo operations
Certain cargoes require the vapour that is displaced by incoming cargo to be returned to the shore facility. The responsible officer should ensure that the ship and the shore vapour system are compatible, and that the system will operate in compliance with local and terminal regulations.
Tanks passed for loading should be tightly secured with all cargo openings closed.
Cargo manifolds should be ready for connection to shore hoses, but with blank flanges removed only on those lines to be used, and only on the connecting side of the ship.

## Slide 7: Ship checks after arrival but prior to cargo operations
Normally tanks to be loaded are pre-inspected for cleanliness by an independent surveyor. This can vary from a superficial visual inspection from the deck, to a very detailed inspection inside the cargo tank in which bulkheads are wall-washed and thoroughly checked. The responsible officer should satisfy himself that the tanks to be so inspected are well ventilated and safe to enter, and are marked as being safe to enter. Tank entry procedures should be complied with. When a tank is entered for inspection the surveyor should be accompanied by the responsible officer or a person delegated by him.
All sighting ports and ullage plugs should be closed and secured, unless expected to be used during handling of the cargo about to be loaded. If openings are required to be open for venting purposes, each opening should be protected by a flame screen designed for that opening and kept clean.

## Slide 8: Ship checks after arrival but prior to cargo operations
When not in use, sea suction and overboard discharge valves connected to cargo and ballast systems must be securely closed and lashed, and may be sealed by shore authorities. In-line blanks should be inserted where these are provided. When lashing is not practicable, valves should be suitably marked to indicate clearly that they are to remain closed.
Before cargo handling is started, all deck scuppers and any open drains onto the jetty must be effectively plugged to prevent spilled cargo escaping into the water around the tanker or onto the terminal. Accumulations of rainwater should be drained periodically and scupper plugs replaced immediately afterwards. Contaminated water should be transferred to a slop tank or other suitable receptacle.

## Slide 9: Ship checks after arrival but prior to cargo operations
Accommodation doors and portholes overlooking the cargo area should be shut. If stern loading is to be undertaken, it may be necessary to provide special advice to the crew.
The cargo venting system should be appropriate for the cargo operation.
Intakes for central air conditioning and mechanical ventilation systems should be checked for correct setting.

## Slide 10: Ship checks after arrival but prior to cargo operations
Means should be provided for the prompt removal of any spillage on deck.
Fire fighting equipment should be inspected, and ready for immediate use.
Correct personal protective clothing and breathing apparatus, appropriate to the cargo, should be immediately available, and should be worn as necessary.

## Slide 11: Ship checks after arrival but prior to cargo operations
Just prior to commencing cargo transfer, the responsible officer should check that the cargo pipeline system is set correctly, that correct valves are open and that pipeline valves not being used (including drop valves) are closed.
A liaison meeting should be held with the responsible terminal staff, at which the operational plan for the order of cargo handling can be agreed. The following joint ship and shore checks in co-operation with a terminal representative are recommended:

## Slide 13: Ship checks after arrival but prior to cargo operations
1.That the Ship/Shore Safety Checklist has been completed satisfactorily.
2. That local and terminal regulations have been ascertained and are being observed.
3. That agreement has been reached with the responsible terminal representative about signals to indicate stand-by, start operation, slow down and stop operation.
4. That when shore-supplied nitrogen is to be used for inerting cargo tanks, the procedure for handling it has been agreed.

## Slide 14: Ship checks after arrival but prior to cargo operations
5. That the sequence of cargoes and pumping rates has been agreed.
6. Whether ship or shore will order pumps to be stopped on completion.
7. That emergency shutdown procedures, and action to be taken in case of fire or other emergency, have been agreed.
8. That if an insulating flange is used in the hose connection, its insulation has not been impaired.

## Slide 15: Safety
HAZARDS
PERSONNEL AND HEALTH
REACTIVITY HAZARDZ
MEDICAL TREATMENT
ATMOSPHERE EVALUATION
GENERAL SAFETY REGULATION

## Slide 16: HAZARDS
Hazards to health, posed by chemical cargoes in tankers are :
Toxicity
A toxic substance (poison) is one which, when absorbed into the human body by ingestion, absorption or inhalation,
produces a serious or fatal effect i.e. it is hazardous to human health.
Asphyxia
Is the restriction of supply of oxygen to the body, how-so-ever caused.
Asphyxia may be caused by a number of reactions produced when a person comes into
contact with different
chemicals:
a) Blockage of air passage by vomit, blood or secretions.
b) Obstruction of the air passage through spasm of air tubes.
c) Fluid in the lung air spaces caused by irritant fumes.
d) Poisoning of the blood which prevents its binding with and carriage of oxygen into the
body.
e) Poisoning of the mechanism of breathing in the chest or brain.
f) Gases that do not support life because they replace or displace oxygen in the
atmosphere.

## Slide 17: HAZARDS
Corrosivity
A substance which completely or partly destroys human tissue, causing serious damage which may be permanent.
Toxic chemicals may enter the body through inhalation, ingestion or absorption through the skin. The harmful effect of a cargo is dependent upon both its physical and chemical properties. The inhalation hazard is primarily dependent upon the cargoes volatility, the more volatile the cargo the greater the quantity of fumes emitted.
Poisoning
A typical case of poisoning involves 3 stage of illness:
1. The latent Stage – is the time between the entry of the poison into the body and the first signs or symptoms are apparent.

## Slide 18: HAZARDS
2. The Active Stage – when the signs and symptoms are apparent. The general symptoms of poisoning include:
headaches , Nausea& vomiting , drowsiness , change in mental behavior , unconsciousness ,
convulsions& pain.
3. The Late Stage – where , if the degree of exposure was small , the patient will start to
recover, and the symptoms will usually reduce in severity.

## Slide 19: HAZARDS
General symptoms of asphyxia are :
- Difficulty in breathing with initial increase in the rate.
- Rapid pulse rate
- Blueness of the skin
- Agitated attitude
- Unconsciousness
Pupils of the eyes react to light

## Slide 20: PERSONNEL AND HEALTH
In the event of accidental leakage, emergency inspection or maintenance tasks, personnel
may be exposed to liquid or gaseous products and it is the purpose of this chapter to review the hazards to personal safety and health which such circumstances may present and to out line the means of hazard avoidance.

## Slide 21: PERSONNEL AND HEALTH
Chemical tanker cargoes may be divided into four groups:
- Petrochemicals
- Alcohols and carbohydrates
- Vegetable and animal oil& fats
Acids and inorganic chemicals
Broadly , the hazards of chemical cargoes or their vapours may be fourfold - asphyxia, toxicity, low temperature and
flammability, while asphyxia , low temperature and flammability apply to all chemical cargoes, the hazard of toxicity applies to only some of them.

## Slide 22: PERSONNEL AND HEALTH
Narcosis , which results in interference with or inhibition of normal responses and control.
sensations are blunted, movements become clumsy and reasoning is distorted prolonged and deep exposure to a narcotic may result in
anesthesia (loss of consciousness). while a victim removed from narcotic exposure will generally fully recover, the danger is that while under the influence he will not respond to normal stimuli and be
oblivious of danger.
Short or long term or even permanent damage to the body tissue system. with some chemicals this may occur at low
levels of concentration if exposure is prolonged and frequent.

## Slide 23: PERSONNEL AND HEALTH
Threshold limit values (TLV)
As a guide to permissible vapour concentrations for prolonged exposure, such as might occur in plant operation.,
various governmental authorities publish of threshold limit value ( tlv) for the toxic substances most handled by industry. the recommended tlvs are updated annually in the light of experience and increased knowledge .
chemical burns

## Slide 24: PERSONNEL AND HEALTH
chemical burns
Skin contact with chemical materials will cause damage similar to that when contact is made with hot materials of similar temperature difference . clearly, there are such hazards in plant operation or on a ship handling chemicals, while containment materials for fully pressurized handling of chemicals will generally be safe at or near ambient temperature.
Some cargoes cause chemical burning, while the rapid evaporation of chemical will minimize the extent of chemical burning on the skin, are especially dangerous to eyes.

## Slide 25
Flammability
Combustion is a chemical reaction, initiated by source of ignition, in which a flammable vapour combines with oxygen in suitable proportion to produce carbon dioxide, water vapour and heat.
The three requirements for combustion to take place are fuel, oxygen and ignition. The proportions of flammable vapour to oxygen or to air must be within the flammable limits.
the gases produced by combustion are heated by the combustion reaction. In open, unconfined spaces the consequent expansion of these gases is unrestricted and combustion reaction may proceed smoothly without undue over pressures developing

## Slide 26: Flammability
if the free expansion of the hot gases is restricted in any way, pressures will rise and the speed of flame travel will increase, depending upon the degree of confinement encountered. Increased flame speed in turn gives rise to more rapid increase in pressure and the combustion can take on the nature of an explosion.
The term flammable range gives a measure of the proportions of flammable vapours to air necessary for combustion to be possible.

## Slide 27: REACTIVITY HAZARDS
Cargoes may undergo chemical reaction during cargo handling or during carriage. The reaction may produce heat, cause the release of large volumes of vapour, an increase in pressure or form harmful and / or flammable vapours.
a) Self reaction or reaction with air
Polymersion is a common reaction, normally prevented by adding an inhibitor to the
cargo and/or inerting the ullage spaces.

## Slide 28: REACTIVITY HAZARDS
b) Reaction as a result of mixing one chemical with another
Neutralisation as a result of mixing an acid with an alkali is a typical example.
c) Reaction as a result of mixing with water
Requires double separation between cargo and any water (ballast or sea) plus special tank cleaning solution.

## Slide 29: MEDICAL TREATMENT
The symptoms and medical treatment recommend for casualties involving asphyxia, narcosis and/or toxic irritation
involves the removal of the casualty from exposure, the application where necessary of artificial respiration , external cardiac massage and the administration of oxygen.
Professional medical treatment should always be sought in cases where casualties have been overcome by toxic and/
or irritant vapours. it is extremely important to label the patient adequately before removal from the ship or terminal . if the finger or hand has been burned, the casualty should hold his hand under his armpit the affected part should then be placed in warm water at about 42 c.
if this is not practicable, then the casualty should be

## Slide 30: MEDICAL TREATMENT
wrapped in blankets and the circulation should be allowed to re-establish itself naturally.
If possible, the casualty should be encouraged to exercise the affected part while it is being warmed, blisters should never be cut or opened, nor clothing removed if it is adhering firmly. The entire affected area should be covered with sterile dressings otherwise , the treatment should be as for hot burns.
Chemical burns can be caused by ammonia,

## Slide 31: MEDICAL TREATMENT
and propylene oxide symptoms are similar to thermal burns, but chemical burning is particularly damaging to the eyes. the affected area should be washed copiously with fresh water for about 10-15 minutes, and then covered either with a sterile dressing. Otherwise, the treatment is as for thermal burns full details of which are contained in the IMO medical first aid guide for use in accidents involving dangerous goods.
Further First-aid procedures for accidents involving hazardous cargo can be found in: the International Chamber of Shipping (ICS) Cargo Data Sheets , the Chemical Hazard Response Information Service
(CHRISS), the Chemical Data Guide for Bulk Shipment by water and IBC code.

## Slide 32: ATMOSPHERE EVALUATION
As previously indicated, it is always preferable to achieve a gas-free condition in a tank or enclosed space prior to entry by personnel. Entry into tanks where this is not possible should only be permitted in exceptional circumstances and when there is no practical alternative, in which case breathing apparatus (and if necessary, protective clothing) must be worn.

## Slide 33: canister filter respirators
These consist of a mask with a replaceable canister filter attached through which contaminated air is drawn by the normal breathing of the wearer. they are simple to operate and maintain, can be put on quickly and have been used extensively as personal protection for emergency purposes on ships certified for carrying toxic cargoes. they are,however, only suitable for relatively low concentrations of gas, once used there is no simple means assessing the remaining capacity of the filter, filter materials are specific to a limited range of gases and, of course, the respirator gives no protection in atmospheres of reduced oxygen content. for these reasons, the IMO code requirement for emergency escape protection is now usually met by lightweight portable packaged self contained breathing apparatus.

## Slide 34: compressed air breathing apparatus
In the self- contained version (SCBA) , the wearer carries his air for breathing in a compressed air cylinder at an initial pressure. the pressure is reduced at the outlet from the cylinder and fed to the faced mask as
required through a demand valve providing a slight positive pressure within the mask. working duration depends upon the capacity of the
air cylinder and the respiratory demand. indicator and alarm features are usually always provided to warn of air supply depletion.
A typical set, providing approximately 30 minutes operation with physical exertion, may weigh considerable amount and the bulk of the cylinder on the back of the wearer imposes some restriction on his maneuverability in confined spaces.

## Slide 35: oxygen resuscitators
This equipment is to provide oxygen enriched respiration to assist the recovery of victims overcome by oxygen deficiency or toxic gas.
Modern equipment are sufficiently portable to be taken into enclosed spaces to give immediate. treatment to the casualty and consists of face mask, pressurized oxygen cylinder and automatic controls to avoid damage to victim and give audible warning in the event of airway obstruction.

## Slide 36: protective clothing
In addition to breathing apparatus full protective clothing should be worn when entering an area where contact with cargo is a possibility. Types of protective clothing vary from those providing protection against liquid splashes to a full positive pressure gas- tight suit will normally incorporate helmet , gloves and boots. Such clothing should also be resistant to low temperatures and solvents. Full protective clothing is particularly important when entering a space which has contained toxic chemicals such as ammonia, propylene oxide.

## Slide 37: protective clothing
For the protection of crew members who are engaged in loading and discharging operations, suitable protective equipment consisting of large aprons, special gloves with long sleeves, suitable footwaer, coveralls of chemical-resistant material, and tight fitting goggles or face shields or both should be available on board. Work cloths and protective equipment should be kept in easily accessible places and in special lockers. Such equipment should not be kept within accommodation spaces, with the exception of new, unused equipment and equipment which has not been used. since undergoing a thorough cleaning process For further information refer to chapter of Personnel protection in IBC code.

## Slide 38: GENERAL SAFETY REGULATION
The handling of chemical cargoes requires that operators always exercise a maximum degree of safety, the overall safety of personnel, machinery and ship demands that everybody on board is thoroughly familiar with the hazards
involved it is the responsibility of each person on board to know the emergency procedures and related routines as
they are prescribed by the master of the ship.
The following check list contains brief rules regarding safety on board, each rule will be explained more fully later in
this chapter.

## Slide 39: GENERAL SAFETY REGULATION
a. Smoking and all use of open fire is only allowed inside the living quarters.
a. Smoking in bed is not allowed.
b. Smoking or use of open fire is not allowed in any part of the ship during loading and discharge operations. Any exemption from this rule may be given by the master only.
c. The deck and all rooms must be kept clean and not be used to store refuse. spilt oil must be removed immediately.
Cleaning rags, etc. must be put into approved steel containers.
d. Shoes must not be fitted with steel reinforcements which may cause sparks.
e. Care must be taken to avoid sparks when using tools in the cargo tank area.
NOTE: Experiments have shown that sparkles tools can cause sparks with sufficient energy to ignite explosive gas mixtures.

## Slide 40: GENERAL SAFETY REGULATION
f. Only explosion proof torches must be used in the cargo tank area
g. The atmosphere inside the hold and cargo tanks must be analyzed and found free of gas prior to entering that area. attempts must be made to detect any local gas concentrations.
Unless a confined space is considered completely ventilated and free of gas, gas masks and air bottles must be used. in addition, personnel who enter such areas must be equipped with ropes or life lines which are supervised by at least two persons situated outside the danger area. note that ordinary gas masks are useless where the oxygen concentration is too low.
h. Clothes that are made of synthetic textiles can cause sparks, especially when used with shoes made from insulating material.
i. Every one must do his utmost to ensure that the safety of crew and ship is not jeopardized.

## Slide 41: IBC CODE
THE INTERNATIONAL CODE FOR THE CONSTRUCTION AND EQUIPMENT OF SHIPS CARRYING DANGEROUS CHEMICALS IN BULK (IBC CODE)
CONTAIN 21 Chapter .
INTERNATIONAL CERTIFICATE OF FITNESS FOR THE CARRIAGE OF DANGEROUS CHEMICALS IN BULK
ATTACHMENT TO THE INTERNATIONAL CERTIFICATE OF FITNESS
Conditions of carriage