## Slide 1
Coastal Navigation
Session 6
Part 1 Distance from a landmark (Chapter 15) a. With a hand bearing compass or pelorus b. With a vertical sextant c. with a horizontal sextant
Part 2 GPS and Electronic Charts (Chapter 16) a. Accuracy b. Limiting factors c. Displays d. Electronic charts (Raster; Vector)
Dominique Prinet www.MarineNavigationBooks.com June 2020

## Slide 2: 1. Distance from a landmark
a. Using a hand bearing compass, a pelorus, or an Automatic Direction Finder (ADF)
Fig. 15.1 (left half)
Doubling the bearing, e.g. from 30° to 60°:
Distance from the landmark (BC)
= distance travelled by the boat (AB)

## Slide 3
Fig. 15.1 (right half)
Doubling the bearing, e.g. from 45° to 90°:
Distance from the landmark (BC)
= distance travelled by the boat (AB)

## Slide 4
Fig. 15.2
Distance from the landmark ≈
6 times the distance travelled (A-B)
for a change of bearing of 10°.

## Slide 5
b. Using a vertical sextant
Fig. 15.4
Fig. 15.5
d = h / tg α
Measure α with a vertical sextant;
read “tg α” off a trigonometric table; and
read “h” off the marine chart.
Without trigonometry table, use the formula:
d (in NM) = [height of landmark in m] x 1.85
angle α in minutes of angle
Valid for small angles α.

## Slide 6
The boat position can be determined from a distance to the landmark (circle of position, vertical sextant), and a bearing (hand-bearing compass)
Fig. 15.6

## Slide 7
c. Using a horizontal sextant
Fig. 15.7
Fig. 15.8
The circle of position from which two landmarks can be seen at a given sextant angle (e.g. 30°, Fig. 15.7) is centered at the intersection of two radii drawn at
α = (90° - sextant angle = 90° - 30° = 60° in this example) off the base line linking the two landmarks (Fig. 15.8).

## Slide 8
Fig. 15.9
Fig. 15.10
The boat position can be established from:
a circle of position (horizontal sextant) and a bearing (hand-bearing compass, Fig. 15.9) or
from two circles of position (horizontal sextant, Fig. 15.10) using three landmarks

## Slide 9: 2. GPS; Electronic charts
Under the best conditions (see limiting factors, next slide), the horizontal accuracy of the GPS system is approximately 3 to 8 metres 95% of the time
The use of the Wide Area Augmentation System (WAAS), which provides corrections through a geostationary satellite, is one way to increase accuracy. Differential GPS, sending local corrections via ground transmitters close to US and Canadian shorelines, is another way.
Vertical accuracy is considerably lower.
The new European “Galileo” system (with partial implementation in 2017) will provide increased accuracy.
a. Accuracy

## Slide 10
Ionospheric and tropospheric interference
Satellite positioning
Calculating ability and accuracy of the GPS unit
Multipath signals; Natural or artificial interference
Horizontal chart datum and chart reliability
Disappearance of details in vector charts at small scales
Loss of signal due to accidental disconnection
Loss of signal due to automatic cut-off at slow speed
b. Limiting factors of the GPS

## Slide 11
Satellite page
c. Displays
Fig. 16.1
Note satellite 09 is too close to NW horizon

## Slide 12
Waypoints and Routes (1/2)
Fig. 16.2

## Slide 13
Waypoints and Routes (2/2)
Fig. 16.3
Note route segments displaying course direction and distance

## Slide 14
Tracks (1/2)
Fig. 16.4
Continuous track

## Slide 15
Tracks (2/2)
Fig. 16.5
Tracks with dots at specific time intervals

## Slide 16
Cross Track Error (1/2)
Fig. 16.6
The intended track is vertical, at the center of the screen.
“Turn to starboard” to get back on track (green arrow), because:
The boat is a little to the left of the intended track (red arrow)
The boat 0.081 NM to the left of the intended track (bottom right window)
The course of the boat over ground (track) is 261˚M (left window), but the next waypoint is further to starboard, at a bearing of 277˚ M (top left window)

## Slide 17
Cross Track Error (2/2)
Fig. 16.7
The boat track is oriented straight up (vertical line, top of dial)
The track over ground is 047˚ (T or M; reading on top of dial, and bottom window).
“Turn to starboard” to get back on track (big black arrow), because:
The boat is 72.5 feet Left (“L”) off the intended track (second window from bottom)
The next waypoint is slightly to starboard, at a bearing of 060˚ (T or M; middle window)

## Slide 18
Raster chart (1/3)
d. Electronic charts
Fig. 16.8
The Vancouver area is on two different raster charts

## Slide 19
Raster chart (2/3)
Fig. 16.9
Part of the previous raster chart blown up (by zooming) to show Vancouver harbour: no additional details are provided; very fuzzy image.

## Slide 20
Raster chart (3/3)
Fig. 16.10
Additional details can only be obtained from a different raster chart, with a much larger scale.

## Slide 21
Vector charts (1/2)
Fig. 16.11
Vector chart read on a laptop, with navigation software (top and left edges).

## Slide 22
Vector charts (2/2)
Fig. 16.12
Part of the previous vector chart blown up (by zooming) to show Vancouver harbour: all available details are provided. The writing remains perfectly readable, with the characters retaining the same size.

## Slide 23
End of Session 7